## Slide 1: VEGETABLE PRODUCTION IN GREENHOUSES

## Slide 2: Greenhouse
A greenhouse is a closed construction with the following characteristics:
It is covered with a material which is transparen to the photosynthetically active radiation,
Its height is sufficient for a human to enter in standing position,
It aims at modifying the inside microclimate with reference to the external environment,
It is used to enable plant cultivation, irrespective of the external climatic conditions.

## Slide 3: Greenhouse effect owing to the closed construction. I. Selective transmittance of the covering material
The transparent covering material is permeable to the ultraviolet, (>400 nm) visible (PAR: 400-720), far-red (720-780) and infra-red radiation (740-2.500 nm)
However the permeability of the transparent covering materials to thermal radiation higher than 2.500 nm is very low or even zero .

## Slide 4: Greenhouse effect owing to the closed construction. II. Obstruction of air exchange
ΙΙ. Temperature, air humidity, and air composition inside the greenhouse are modified because the air exchange with the external environment is drastically restricted.

## Slide 5: Area and production of greenhouse vegetables in Greece (2012)
Crop species | Tall greenhouses |  |  |  |  |  |  |  |  |  | 2nd crop | 
 | Heated greenhouses |  |  |  | Unheated greenhouses |  |  |  | Total (tall greenhouses) |  |  | 
 | Glasshouses |  | Plastic-covered greenhouses |  | Glasshouses |  | Plastic-covered greenhouses |  |  |  |  | 
 | area (ha) | prod. (ton) | area (ha) | prod. (ton) | area (ha) | prod. (ton) | area (ha) | prod. (ton) | area (ha) | prod. (ton) | area (ha) | prod. (ton)
Tomato | 62.2 | 11,203 | 425.2 | 41,165 | 23.9 | 2,510 | 1,393.0 | 164,161 | 1,904.3 | 219,039 | 710.9 | 71,059
Cucumber | 11.5 | 1,405 | 188.3 | 28,578 | 25.4 | 5,280 | 895.5 | 93,178 | 1,120.6 | 128,441 | 317.9 | 38,582
Zucchini | 0.9 | 41 | 15.0 | 729 | 3.0 | 240 | 57.4 | 2,137 | 76.3 | 3,147 | 31.8 | 866
Eggplant | 0.7 | 56 | 16.0 | 968 | 3.0 | 220 | 155.8 | 16,884 | 175.6 | 18,128 | 12.3 | 754
Pepper | 11.9 | 1,570 | 78.9 | 4,935 | 8.3 | 716 | 626.9 | 71,132 | 725.9 | 78,353 | 52.8 | 3,411
Bean | 2.0 | 50 | 62.2 | 1,978 | 7.5 | 260 | 104.4 | 2,167 | 176.1 | 4,455 | 125.9 | 3,378
Lettuce | 1.8 | 63 | 22.4 | 634 | 3.0 | 120 | 115.8 | 2,489 | 143.0 | 3,306 | 237.8 | 4,704
Melon | 0.1 | 0 | 2.1 | 85 | 1.0 | 20 | 2.0 | 100 | 5.2 | 205 | 118.0 | 8,400
Watermelon | 0.2 | 0 | 1.6 | 96 | 6.0 | 420 | 14.5 | 620 | 22.3 | 1,136 | 685.0 | 39,150
Strawberry | 0.0 | 0 | 0.0 | 0 | 0.0 | 0 | 1,163.0 | 43,927 | 1,163.0 | 43,927 | 2.0 | 60
Miscellaneous | 2.0 | 0 | 16.9 | 1,135 | 1.0 | 15 | 42.1 | 772 | 62.1 | 1,922 | 50.9 | 1,005
Total | 93.3 | 14,388 | 828.6 | 80,301 | 82.1 | 9,801 | 4,570.4 | 397,568 | 5,574.3 | 502,058 | 2,345.2 | 171,368

## Slide 6: Types of greenhouses
Modern greenhouse combined with hydroponics, resulting in high yields, which requires a high investment.
Simple construction: Low cost resulting in low yield. Very common GH type in Mediterranean countries.

## Slide 7: Construction characteristics of greenhouses
Greenhouse shape
Greenhouse width
Greenhouse height
Greenhouse structure
Greenhouse covering materials

## Slide 8: Greenhouse shapes
α
β
γ
δ
ε
στ
Round arched tunnel
Round arch with vertical side wall
Saddle roof
Shed roof
Pointed arch with sloping side wall
Pointed arch with vertical side wall

## Slide 9: Structure of a greenhouse

## Slide 10
Single-line greenhouse
Multiple-line greenhouse

## Slide 11: Round arched tunnel

## Slide 12: Round arch with vertical side wall

## Slide 13: Saddle roof with one roof per construction unit (wide-span type)

## Slide 14: Saddle roof with two roofs per construction unit (Venlo type)

## Slide 15: Pointed-arched (gothic-arched) structures with sloping side wall

## Slide 16: Pointed arched (gothic-arched) with vertical side walls

## Slide 17: Greenhouse height
High constructions (7-7.5 m) are suggested
Advantages:
Larger volume per area unit and thus a higher buffering to temperature changes during the 24-hours cycle.
A lower fluctuation in CO2 concentrations during the 24-hours cycle.
More vertical space for the development of high plants

## Slide 18: Greenhouse orientation
Date | East - West | North - South
January 2 | 379 | 293
January 4 | 426 | 322
February 6 | 578 | 530
March 10 | 1,243 | 1,226
April 14 | 1,955 | 2,104
June 20 | 2,720 | 2,969
Impact of greenhouse orientation on daily PAR interception (Wh m-2) in Dutch greenhouses at different dates during the year.
PAR transmittance through two similar greenhouses at the same location differing in the orientation
.
Transmittance to PAR (%)
21 Dec. 21 Febr. 21 Apr. 21 June
E-W
N-S

## Slide 19: Structure material
Wood
Galvanised steel
Aluminum

## Slide 20: Greenhouse covering materials
Three groups of covering materials are used in greenhouse:
soft plastic,
rigid plastic,
glass.

## Slide 21: Special types of plastic covering sheets
Stabilized sheets
UV-blocking plastic sheets
IR-radiation blocking plastic films
Plastic films reflecting the NIR radiation
Plastic films increasing the diffusion of the solar radiation
Ant-drop plastic films
Anti-fog plastic films

## Slide 22: Increase of light transmittance by using anti-drop films

## Slide 23: Greenhouse equipment
Ventilation systems
Heating and energy saving systems
Dehumification systems
Shading systems
Cooling systems
Carbon dioxide (CO2) enrichment systems
Artificial lighting systems

## Slide 24: Natural ventilation by opening ventilators at side walls, gables ridge or roof area
Flap ventilators
Roll-up ventilators

## Slide 25: Forced ventilation by fans
Συστήματα δυναμικού εξαερισμού

## Slide 26: Insect-proof screens
Thrips White fly Aphids

## Slide 27: Impact of insect proof screens on greenhouse ventilation

## Slide 28: Heating and energy saving systems
They are distinguished according to the following characteristics:
Heat (energy) source
Heat generator (heating system)
Heat distribution system.

## Slide 29: Energy source for heating
Combustion of fossil fuels, oil, gas, coal
Combustion of biomass (wood, straw, husks, etc.)
Geothermal energy
Waste heat from industry
Solar energy

## Slide 30: Heating systems
Central warm water boiler
Directly fired air heater
Central warm water boiler
Decentralised warm water boiler
Directly fired air heater

## Slide 31: Heat distribution systems
Recirculation of warm water via metallic pipes
Recirculation of vapor via metallic pipes
Corrugated plastic tubes for warm water recirculation
Perforated plastic tubes for air heating systems

## Slide 32: Thermal screens
Thermal screens are capable of reducing the energy consumption for heating by 35-40%.
Thermal screens are made of materials with low heat conductivity which reduce the heat exchange between the inside air and the outside environment

## Slide 33: Installation of thermal screens
In most cases they are placed at the top of the greenhouse
In these cases they are used also as shading screens during the summer.
In greenhouse located in cold-climate areas the thermal screens cover also the side walls.

## Slide 34: Shading systems
The shading of the greenhouse is aimed at reducing the income of solar radiation, thereby reducing the greenhouse temperature whenever ventilation is not sufficient in reducing the inside air temperature.
On the other hand, shading affects also two other climatic parameters, i.e.:
The relative humidity which increases with increasing shading
The interception of PAR by plants which may result in yield losses.
Methods of greenhouse shading
Whitening of the covering material
Net shading
Shading screens

## Slide 35: Shading by whitening
Whitening of greenhouses
Impact of whitening on light transmittance
External radiation
Inside radiation before whitening
Inside radiation before whitening
Time (h)
Solar radiation intensity (W m-2)

## Slide 36: Shading screens

## Slide 37: Cooling systems
I. Fog system
A fog cooling system consists of:
a water softener,
good filters to prevent nozzle clogging,
a water reservoir,
pumps,
pressure regulation valves,
tubes with nozzles above the crop.
Prerequisites for high efficiency:
The air must be moving inside the greenhouse,
The air has to be continually renewed through passive ventilators.

## Slide 38: Cooling systems
II. Fan and pad cooling
Air from outside is blown or sucked through pads with a large surface.
The pads are kept permanently wet by sprinkling water that evaporates on the surface of the pad and cools the air down.
The fans suck the air:
either from outside to the inside (positive pressure),
or from inside to the outside of the greenhouse (negative pressure).

## Slide 39: Negative versus positive pressure fan and pad systems
Negative pressure fan and pad system. The fans suck the air through the pad and greenhouse.
Positive pressure fan and pad system. The fans and pads are located on one side and vents on the other side. The fans blow the air through the greenhouse so that an overpressure occurs.
Wet pad
Wet pad
Fan
Fan
Negative pressure fan and pad system
Positive pressure fan and pad system

## Slide 40: Installation of fans and pads in large greenhouse units
The distance between the wet pads and the fans or the vents should not exceed 50-60 m but preferably it is advised to be up to 40 m.
Wet pad
Wet pad
Fans

## Slide 41: CO2 enrichment systems
Technical carbon dioxide kept under pressure in liquid form in bottles or tanks
Exhaust gases from:
gas burner or,
directly fired air heater with gas burner.
Simultaneous heat production takes place.

## Slide 42: CO2 distribution inside the greenhouse
The CO2 is distributed to the greenhouse air via perforated plastic tubes.

## Slide 43: Artificial lighting to increase photosynthetic assimilation
HPS: high-pressure sodium
Υψηλό κόστος εγκατάστασης & λειτουργίας
LED (light emitting diode)